## Slide 1: Surface Plasmon Resonance (SPR) and Quartz Crystal Microbalance (QCM)
Troy Lowry

## Slide 2: The Need for Label-Free Biosensors
have minimal preparation time (quick to setup)
avoid confounding effects of molecular probes
be robust and highly adaptable to a broad array of molecules
Label-Free Biosensors seek to:
Two examples for today: Surface Plasmon Resonance and Quartz Crystal Microbalance

## Slide 3: SPR is a label-free biosensing method that utilizes changes in refractive index in light caused by photon absorption by metal surface plasmons (surface electrons)
The analyte has to be no smaller than 100 g/mol

## Slide 4: History of SPR
Early 1900’s R.M.Wood at Johns Hopkins University noted that dark and light banded patterns arose from polarized light was shone onto metal backed gratings
1950’s Pines and Bohm suggested energy losses due to oscillating, conducting electrons (plasmons)
1960’s Kretschmann and Otto demonstrated optical excitation of surface plasmons by total reflection
1980 – Pharmacia became interested in the technology and by 1984 developed a commercial SPR machine which would become Biacore
https://www.sprpages.nl/spr-overview/spr-history

## Slide 5: Surface Plasmon Resonance – How It Works
SPR limit of detection is roughly 10 pg/mL

## Slide 6: SPR Study of KcsA-Kv1.3
Vaish, A., S. B. Guo, et al. (2018). "On-chip membrane protein cell-free expression enables development
of a direct binding assay: A curious case of potassium channel KcsA-Kv1.3." Analytical Biochemistry 556: 70-77.

## Slide 7
Vaish, A., S. B. Guo, et al. (2018). "On-chip membrane protein cell-free expression enables development
of a direct binding assay: A curious case of potassium channel KcsA-Kv1.3." Analytical Biochemistry 556: 70-77.
Sequencing the chimeric potassium channel

## Slide 8
Vaish, A., S. B. Guo, et al. (2018). "On-chip membrane protein cell-free expression enables development
of a direct binding assay: A curious case of potassium channel KcsA-Kv1.3." Analytical Biochemistry 556: 70-77.
Binding of K-K in the presence of Phosphlipids

## Slide 9
Vaish, A., S. B. Guo, et al. (2018). "On-chip membrane protein cell-free expression enables development
of a direct binding assay: A curious case of potassium channel KcsA-Kv1.3." Analytical Biochemistry 556: 70-77.
Immobilization onto SPR chip
Note: Response Unit is directly proportional to the concentration of biomolecules
on the surface

## Slide 10
Vaish, A., S. B. Guo, et al. (2018). "On-chip membrane protein cell-free expression enables development
of a direct binding assay: A curious case of potassium channel KcsA-Kv1.3." Analytical Biochemistry 556: 70-77.
Binding of complementary antibody to K-K functionalized lipid bilayer

## Slide 11
Vaish, A., S. B. Guo, et al. (2018). "On-chip membrane protein cell-free expression enables development
of a direct binding assay: A curious case of potassium channel KcsA-Kv1.3." Analytical Biochemistry 556: 70-77.
Real time monitory of K-K reaction mix onto anti GFP functionalized SPR surface

## Slide 12
Vaish, A., S. B. Guo, et al. (2018). "On-chip membrane protein cell-free expression enables development
of a direct binding assay: A curious case of potassium channel KcsA-Kv1.3." Analytical Biochemistry 556: 70-77.
Kv1.3 blocker Pap-1 binds to K-K functional lipid extract

## Slide 13
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Tethered Lipid Bilayers onto SPR Chip

## Slide 14
SPR + electrochemical/impedance spectroscopic module
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.

## Slide 15
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.

## Slide 16
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Impedance Spectroscopy

## Slide 17
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Tethered Lipid Bilayer and incorporation of alpha hemolysin

## Slide 18
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Translocation of K+ ions across the lipid bilayer by valinomycin

## Slide 19
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Specific Resistance of valinomycin-doped tethered bilayer lipid membrane

## Slide 20
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Patch clamp of tethered lipid membrane-doped with synthetic M2 (pentameric peptide
that mimics the channel part of the nicotinic acetylcholine receptor protein)

## Slide 21
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Tethered membranes via incorporated proteins!
Histidine loves NTA – this can control
the orientation

## Slide 22
Knoll, W., I. Koper, et al. (2008). "Tethered bimolecular lipid membranes - A novel model membrane platform." Electrochimica Acta 53(23): 6680-6689.
Cell-free expression of membrane proteins with immediate insertion into the tethered lipid bilayer

## Slide 23: Quartz Crystal Microbalance – Types of Publications Referencing It
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.

## Slide 24
What is QCM?
QCM is a biosensor that is based on acoustic transduction, meaning the binding
event (change in mass) is based upon changes in quartz crystal resonance.
It is label-free
Contact mechanics, interfacial dynamics, surface roughness, viscoelasticity, density
and mass monitored in real time

## Slide 25
History of QCM
Sauerbrey in 1959 demonstrated a linear relationship between mass adsorbed to the surface
and the resonant frequency of the crystal in air or vacuum.
QCM was born.
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.

## Slide 26
Typical Experimental Design of QCM
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.

## Slide 27
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.
QCM and Detection Limits for DNA Sequences

## Slide 28
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.
DNA hybridization on an oligonucleotide immobilized QCM biosensor

## Slide 29
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.
Affect of Annexin binding on POPC/POPS membranes

## Slide 30
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.
QCM Detection Limits of Viruses and Phage

## Slide 31
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.
QCM can detect bacteria

## Slide 32
Cooper, M. A. and V. T. Singleton (2007). "A survey of the 2001 to 2005 quartz crystal microbalance biosensor literature: applications of acoustic physics to the analysis of biomolecular interactions." Journal of Molecular Recognition 20(3): 154-184.
QCM Small Molecule Detection

## Slide 33
Application : Olfactory Biosensor Research
Glatz, R. and K. Bailey-Hill (2011). "Mimicking nature's noses: From receptor deorphaning to olfactory biosensing." Progress in Neurobiology 93(2): 270-296.